## Slide 1: NEONAL MECHNICAL VENTILATION

## Slide 2: BACKGROUND
Improve gas exchange, primarily by lung recruitment to improve ventilation/perfusion (V/Q)
Decrease work of breathing
Provide ventilation in infants with respiratory depression or apnea

## Slide 3: Indications for ventilation
Respiratory acidosis, documented by an arterial pH <7.20 and a PaCO2 >60 mm Hg
Hypoxia, documented by an arterial PaO2 <50 mm Hg despite oxygen supplementation of50- 70 percent on nasal CPAP
Severe apnea

## Slide 4: Types of ventilation
Conventional ventilation (intermittent mandatory ventilation (IMV)
High frequency ventilation

## Slide 5: CONVENTIONAL VENTILATION
Time-cycled pressure-limited (TCPL)
Intermittent mandatory ventilation (IMV)
Synchronized mandatory ventilation
pressure support ventilation

## Slide 6: Pressure-limited ventilation
The continuous flow, time-cycled pressure-limited (TCPL) ventilator provides a continuous flow of heated and humidified air and delivers a breath that is set by peak inspiratory pressure (PIP) and either the absolute inspiratory time or inspiratory:expiratory time ratio (I:E ratio).

## Slide 7: Tidal volume
Lung compliance and resistance
Tubing resistance
PIP

## Slide 8: Arteial oxygen saturation
PIP
PEEP
I:E ratio
Fio2

## Slide 9: Mean Airway Pressure
PIP
PEEP
I:E Ratio
Flow

## Slide 10: Arterial co2 pressure
Minute ventilation(respiratory rate ,VT)
PIP

## Slide 11: Synchronized and patient-triggered ventilation
synchronized ventilation:the ventilator delivers an intermittent positive pressure breath at a fixed rate in synchrony with the infant's inspiratory effort.
Assist/Control ventilation: a positive pressure breath is delivered with every inspiratory effort.

## Slide 12: Pressure-support addition to SIMV
Pressure-support ventilation is a patient-triggered, pressure-limited, flow-cycled mode of ventilation. It delivers inspiratory support until the inspiratory flow decreases to a predetermined percentage of its peak value, usually 25 percent.

## Slide 13: Volume-controlled (VC) ventilation
Volume-controlled (VC) ventilation The clinician presets the tidal volume (generally 4 to 6 mL/kg), the respiratory rate, and an inspiratory time limit .
Volume-guarantee ventilation (VG) is a form of time-cycled, pressure-limited ventilation. (Hybrid ventilation)

## Slide 14: HIGH FREQUENCY VENTILATION
High frequency ventilation (HFV) delivers small volumes of gas, which are equal to or smaller than anatomic dead space, at an extremely rapid rate (300 to 1500 breaths per minute).

## Slide 15: NONINVASIVE MECHANICAL VENTILATION
Neonatal nasal intermittent positive pressure ventilation (NIPPV) provides noninvasive respiratory support to preterm infants who otherwise would require endotracheal intubation and ventilation

## Slide 16: Approach
SIMVusing a TCPL ventilator is the initial mode of ventilation in most neonates.
Pressure support ventilation (PSV) is generally reserved for infants with BPD who require long-term ventilator support or are difficult to wean from SIMV.
In premature infants who are treated with surfactant, we use SIMV/volume-guarantee ventilation.

## Slide 17
High frequency ventilation is used as rescue therapy when positive inspiratory pressure (PIP) is equal to or greater than 30 cm H2O or mean air pressure exceeds 10 to 12 cm H2O.
We utilize nasal CPAP for management of apnea of prematurity and early, mild RDS.

## Slide 18: Advantages of Volume Guarantee
Less risk of volutrauma
Reduced peak pressure
More stable tidal volume
Auto-weaning of peak pressure

## Slide 19: VAPS (volume assured pressure support
Combination of PSV and volume target
Flow cycled but inspiration is not terminated till set TV reached
Helps when compliance worsens, patient fatigue
Inspiratory phase gets prolonged

## Slide 20: PRVC(Pressure regulated volume support)
Both features of PC and VC incorporated
1st test breath assess need for pressure to deliver a target TV
Subsequent breaths are pressure controlled to deliver set TV
Pressure and volume changes

## Slide 21: PAV(Proportional assist ventilation
Pressure applied is servo controlled
Increasing proportionally to the inspiratory flow and tidal volume generated by patient
Patient controls frequency,timing,and rate of lung inflation

## Slide 22: MMV(Mandatory minute ventilation
Target minute volume is set
Breaths are spontaneous PSV
If MV is not met, ventilator gives SIMV breath